## Slide 1: Error Correcting Codes for High Altitude Balloons
Matthew Brejza
The author acknowledges the use of the IRIDIS High Performance Computing Facility, and associated support services at the University of Southampton, in the completion of this work

## Slide 2: Why Error Correction Codes are Needed?
Reducing transmitted power
Maintain reliable communication in unfavourable conditions
  Bursts of interference
  Fading signal
  Low SNR
Increase throughput

## Slide 3: Some Error Correcting Codes
Block
  BCH (1960)
  Reed Solomon (1960) CDs/DVDs, DVB-T
  LDPC (1963, 1996) DVB-S2
Convolutional
  Viterbi decoded (1967) DVB-T, deep space
  BCJR decoded (1974)
  Turbo (1993) LTE

## Slide 4: A Very Basic Code
Repetition code
1/3 rate code
Performance: bad
01101
000 111 111 000 111
010 110 111 011 011
01111
+
noise

## Slide 5: An Improvement
-2 | 3 | 1 | -5 | -1
2 | 4 | 5 | 2 | 3
-3 | -2 | 2 | 1 | 2
01101
0 1 1 0 1
0 1 1 0 1
0 1 1 0 1
-3 5 8 -2 4
+
noise
Demod
0 1 1 0 1
channel
Soft information conveys probabilities for each bit
Usually expressed in the log domain, numbers have much smaller dynamic range
  Known as Log Likelihood Ratio (LLR)

## Slide 6: Reed Solomon (RS) Code
Developed in 1960s
Block Code
Non-binary
Adds t parity symbols, can correct up to t/2 symbol errors
Examples
  RS(7,3) – R=0.43, symbol = 3 bits, 4 parity symbols
  RS(255,223) – R=0.87, symbol = 8 bits, 32 parity symbols

## Slide 7: Bit Error Rate (BER) Plot
AWGN channel, BPSK modulation

## Slide 8: Eb/N0 vs. SNR
SNR provides unfair comparison between codes of different rates
Eb/N0 – ‘SNR per data bit’
  Eb/N0 = SNR – 10log10(R)
  Two schemes at the same Eb/N0 use the same energy to transmit a sequence
  Takes into account extra bits that need to be sent
    Either extra bits take more bandwidth
    Extra bits are added on at the end – take more time

## Slide 9: BER - Eb/N0 Plot
AWGN channel, BPSK modulation

## Slide 10: Turbo Code
Combines two convolutional codes
1/3 rate code (min)
  Puncture the output to get desired rate
Uses soft information
Uses iterative decoding

## Slide 11: BER for Turbo Code, Varying Iterations
AWGN channel, BPSK modulation, message length = 992

## Slide 12: BER - Eb/N0 Plot
Turbo Rate ∈ {⅓, 0.5,0.6,0.7,0.8,0.9}
AWGN channel, BPSK modulation, message length = 6144

## Slide 13: Frame Error Rate (FER)
AWGN, BPSK, message length = 992 (turbo & RS(7,3)); 1784 (RS(255,223))

## Slide 14: Capacity
AWGN, BPSK, FER=10-2
Theoretical max throughput for given SNR
Graph shows capacity limit for FER = 10-2

## Slide 15: A Fading Channel
Often swinging or falling payloads produce time fading signals
Simple model produced to test performance in a fading channel

## Slide 16: FER - fading
Fading channel, BPSK, message length = 992 (turbo & RS(7,3)); 1784 (RS(255,223))

## Slide 17: Capacity (Fading)
fading, BPSK, FER=10-2

## Slide 18: Modulation Schemes – BPSK, (M)FSK
AWGN

## Slide 19: Capacity - BPSK, FSK and MFSK
Frequency shift schemes (FSK/MFSK)
  Power efficient
  bandwidth inefficient
Phase/Amplitude shift schemes (BPSK,QAM)
  Power inefficient
  Bandwidth efficient

## Slide 20: Deep Space Code Usage
http://www.ee.caltech.edu/EE/Faculty/rjm/papers/Viterbi70.pdf

## Slide 21: Potential New Telemetry String
Turbo code – R ∈ {⅓, ⅖, ½, ⅔, 1}
Parity bits interleaved and split into four groups
  Send as many as needed depending on stage of flight
Ideally keep the same length (of the data part) throughout flight
Sync + callsign
Length + packet info
GPS
Other telemetry
Sync
Parity 1
Parity 2
Parity 3
Parity 4
Sync + callsign
(next packet)
Send as many as needed
Checksum

## Slide 22: Concluding Remarks
Can vary coding rate depending on conditions
Coding gain allows lower output power, or higher throughput
Improves reliability in challenging conditions (potentially 22dB gain)
Encoder complexity is low

## Slide 23: Questions?
What goes ‘pieces of 7, pieces of 7’?
  A parity error